Title
Gentoo Stage3 Installation Guide
LVM2 and Systemd support included
Aug 13th 2014
Aaron Johnson
QCLUG
www.qclug.com
(Installation steps were taken from the official Gentoo Handbook)

---
Gentoo Handbook
Your Gentoo installation starts with the Handbook located at: https://www.gentoo.org/doc/en/handbook/
Skip straight to: “Choosing the Right Installation Medium”

---
Choose a mirror
- Browse to /releases/amd64/autobuilds/current-iso/
- Download the file labeled install-amd64-minimal-<release>.iso using wget -c

---
Verify media and boot
- Ensure the media is good by running a checksum against the .iso file:
- Save a copy of the corresponding .iso.DIGESTS file to the same directory as the .iso file.
- Run the following command: sha512sum -c <downloaded iso.DIGESTS>
- If the media is good, the first line of output should be: install-amd64-minimal-20140724.iso: OK
- Boot the media and press Enter at the boot: prompt to use the default gentoo kernel (or enter gentoo dosshd to automatically start sshd!)
- Start sshd for ease of installation: /etc/init.d/sshd start
- Also, set the root password so you can login: passwd
- Login from another machine and continue the installation:
  ssh root@<ip_address>

---
Networking configuration
- If your network interface card is a common one it should load automatically during boot via udev
- If DHCP is available then you should be online already
- If a static configuration is nessesary then you use one of the following static configuration methods:
  - Manual method:
    ifconfig eth0 <ip_address> netmask <subnet_mask> up; route add default gw <gw_ip_address>
    Or
  - Wizard method: net-setup eth0
- For advanced network configurations, refer to the “Configuring your Network” section in the Gentoo Handbook:

---
Prepare your disk
3. Create file systems:
1. To see if your disk is detected type: fdisk -l
2. Use fdisk to create an LVM type partition
   start the partition at sector 2048
   (required for GRUB2): fdisk /dev/sda
3. Create a LVM structure like this:
pvcreate /dev/sda1
vgcreate vg00 /dev/sda1
lvcreate -n boot -L512M vg00
lvcreate -n swap -L4G vg00
lvcreate -n root -l100%FREE vg00
4. Mount the new file systems:

---
Installing Gentoo files
- Change directory to where your root filesystem is mounted:
  cd /mnt/gentoo
- Download the Stage3 tarball from a Gentoo mirror using wget:
  wget -c http://www.gtlib.gatech.edu/pub/gentoo/releases/amd64/autobuilds/current-iso/stage3-amd64-20140724.tar.bz2
- Extract the tarball using the following tar flags: tar xvjpf stage3-*.tar.bz2
- Determine your appropriate CFLAGS settings for your specific CPU: http://wiki.gentoo.org/wiki/Safe_CFLAGS
- Select your Gentoo mirrors:
  NOTE: Add the http/ftp mirror only, DO NOT CONFIGURE THE SYNC VARIABLE FOR RSYNC, IT WILL BREAK!
  mirrorselect -i -o >> /mnt/gentoo/etc/portage/make.conf
- Configure DNS:
  cp -L /etc/resolv.conf /mnt/gentoo/etc/

---
Bind mount and chroot
- Before we can chroot, we must bind mount several important filesystems:
  mount -t proc proc /mnt/gentoo/proc
  mount --rbind /sys /mnt/gentoo/sys
  mount --rbind /dev /mnt/gentoo/dev
- chroot, load /etc/profile, and set your PS1:
  chroot /mnt/gentoo /bin/bash
  source /etc/profile
  export PS1="(chroot) $PS1"
- Grab the latest portage snapshot:
  emerge-webrsync
- Update the portage tree:
  emerge --sync

---
Build-time customizations
Choose your Gentoo System Profile:
eselect profile list
eselect profile set 5 #(GNOME with systemd)
Before setting your CFLAGS, install the boost-build package as there is a bug that may prevent you from installing it:
LDFLAGS="--verbose" emerge -va1 dev-util/boost-build
Be cautious of the below options. These settings can make compilation of certain packages difficult if not impossible...
Add CFLAGS settings to: /etc/portage/make.conf
Also add MAKEOPTS to make.conf (core count +1): MAKEOPTS="-j3"
Set your USE flags (Example below should work for KDE or GNOME systems):
USE="bindist mmx sse sse2 X dbus gtk gnome qt4 kde"

---
Systemd and LVM2
- Install and configure LVM2:
  echo "sys-fs/lvm2 static" >> /etc/portage/package.use
  emerge sys-fs/lvm2
  nano -w /etc/lvm/lvm.conf
  #Set use_lvmetad to '1' for systemd
  use_lvmetad = 1
  nano /etc/genkernel.conf
  LVM=”yes”
  rc-update add lvm boot
- Install and configure Systemd:
  USE="-systemd" emerge sys-apps/dbus
  ln -sf /proc/self/mounts /etc/mtab
  nano -w /etc/portage/make.conf
  # add systemd to USE flag
  emerge sys-apps/systemd
  systemctl enable lvm2-monitor.service

---
Timezone and locale
- Set your timezone:
  ls /usr/share/zoneinfo
  echo "America/Chicago" > /etc/timezone
  emerge --config sys-libs/timezone-data
- Configure locales:
  nano -w /etc/locale.gen
  en_US ISO-8859-1
  en_US.UTF-8 UTF-8
  locale-gen
- Set system-wide locale settings:
  eselect locale list
  eselect locale set 4 #en_US.utf8
- Reload shell environment:
  env-update && source /etc/profile

---
Kernel configuration
- Install the kernel sources:
  emerge gentoo-sources
- Choose your kernel installation method:
  - If you want full customization, follow the manual kernel installation steps here: https://www.gentoo.org/doc/en/handbook/handbook-amd64.xml?part=1&chap=7#manual
  - The quick and easy way is to use genkernel which is documented below:
- Install the genkernel script with Systemd support:
  emerge genkernel-next
- Configure fstab:
  nano -w /etc/fstab
  /dev/vg00/boot /boot ext4 noauto,noatime 1 2
  /dev/vg00/root / ext4 noatime 0 1
  /dev/vg00/swap none swap sw 0 0
- Compile the kernel:
  genkernel --udev --lvm all

---
System configuration
- Set your hostname and domainname:
  nano -w /etc/conf.d/hostname
  hostname="tux"
  nano -w /etc/conf.d/net
  dns_domain_lo="homenetwork"
- Configure networking:
  emerge --noreplace netifrc
  emerge dhcpcd
  nano -w /etc/conf.d/net
  config_eth0="dhcp"
- Auto-start networking at boot:
  cd /etc/init.d
  ln -s net.lo net.eth0
  rc-update add net.eth0 default
Update /etc/hosts:
nano -w /etc/hosts
127.0.0.1 tux.homenetwork tux localhost
Set the root password:
passwd
Set the keymap variable:
nano -w /etc/conf.d/keymaps
Set the clock variable:
nano -w /etc/conf.d/hwclock
clock="local"

---
Install System Tools
(optional)
- Install syslog-ng:
  emerge syslog-ng
  systemctl enable syslog-ng
- Install cron:
  emerge cronie
  systemctl enable cronie
- Install locate:
  emerge mlocate
- Enable sshd:
  systemctl enable sshd

---
Bootloader configuration
- Install GRUB2:
  echo "sys-boot/grub:2 device-mapper" >> /etc/portage/package.use
  emerge sys-boot/grub
  echo "GRUB_PRELOAD_MODULES=lvm" >> /etc/default/grub
  echo "GRUB_CMDLINE_LINUX="dolvm rootfstype=ext4 real_init=/usr/lib/systemd/systemd" >> /etc/default/grub
  grub2-install /dev/sda
  grub2-mkconfig -o /boot/grub/grub.cfg
- Create initramfs:
  genkernel --lvm --udev initramfs